## Slide 1
August 7-9, 2017
Matthew Dahlhausen
Mostapha Sadeghipour Roudsari
Chris Mackey
Theo Armour
An interactive workshop on open source web tools to use in your simulation practice
Introduction to Open Web Tools MiniWorkshop

## Slide 2
Outline:
  Examples (25 min)
    Mostapha :: epwmap
    Matt :: epwvis
    Chris :: Payette Thermal Comfort Tool
    Theo :: ladybug-web
  Workshop (40 min)
    Choosing a language for your project
  Closing & Questions (10 min)

## Slide 3: Examples (25 min)
What was the goal of the tool?
Who do you imagine using it?
Which languages did you use, and why that language?
How long did it take, and what were some lessons learned?
What could you do to improve the tool?

## Slide 4: epwmap ladybug.tools/epwmap d3.js, google maps

## Slide 5
An online viewer and analysis tool for EnergyPlus Weather (EPW) files
epwvis

## Slide 6: epwvis https://mdahlhausen.github.io/epwvis/ d3.js

## Slide 7: epwvis
Motivation:
    Lots tools that will give fixed graphics for a particular place
    I wanted to be able to do quick analysis without a spreadsheet
    For simple questions:
    - how many hours per year can I do waterside economizing?
    - what is a typical temperature range during occupied hours in summer?
Drag & Drop
Analysis

## Slide 8: epwvis
Picked javascript / d3.js because:
              (1) browser based (anyone can use)
              (2) interaction
              (3) low-level graphics for control
              Steps broken down:
              Parse .epw file with javascript
              Setup page layout
              Add basic floodplot (proof of data import)
              Add SI/IP units conversions
              Add crossfilter analysis
              Add Windrose

## Slide 9: epwvis
↑ Convert this
Into this →
Notes: Data parsing

## Slide 10: epwvis
Lessons Learned:
Web languages often library dependencies – need to trade-off using libraries vs. keeping page simple and lean
Need to think a bit about data parsing – minimal steps to go fast
Organize structure from the beginning to save time later repeated tasks. E.g., each type of graph is a function, pass parameters to it.
Having live-feedback is very useful for speed. It WON’T work the first time.
Future:
More analysis, filtering, graph options, save to image, custom layouts

## Slide 11
A tool to eliminate perimeter heat in the building industry
Glazing and Thermal Comfort Tool

## Slide 12: Glazing and Winter Comfort Tool http://www.payette.com/building-science/glazing-and-winter-comfort-tool d3.js, bootstrap

## Slide 13: PERIMETER HEAT

## Slide 14: If this were well insulated PERIMETER HEAT

## Slide 15: We wouldn’t need this If this were well insulated PERIMETER HEAT

## Slide 16: We wouldn’t need this If this were well insulated $10,000 CFD Simulation That took 2 weeks Found comfortable conditions with triple pane PERIMETER HEAT

## Slide 17: We wouldn’t need this If this were well insulated PERIMETER HEAT
 | Cost/ft2 Window
Upgrade Double to Triple Pane | $5.47
Add Perimeter Heat to Double | $53.20

## Slide 18: Degrading your Window U-Value by Heating the Inner Surface PERIMETER HEAT

## Slide 19: CAUSES OF WINTER DISCOMFORT

## Slide 20: Radiant Discomfort (Full-body Discomfort) Draft Discomfort (Ankle Discomfort) CAUSES OF WINTER DISCOMFORT

## Slide 21: Radiant Discomfort (Full-body Discomfort) Window View Factor Window Temperature (U-Value) Causes CAUSES OF WINTER DISCOMFORT

## Slide 22: Radiant Discomfort (Full-body Discomfort) CAUSES OF WINTER DISCOMFORT

## Slide 23: Draft Discomfort (Ankle Discomfort) Window Height Window Temperature (U-Value) Causes CAUSES OF WINTER DISCOMFORT

## Slide 24: Draft Discomfort (Ankle Discomfort) CAUSES OF WINTER DISCOMFORT

## Slide 25: EVOLUTION OF A TOOL

## Slide 26: EVOLUTION OF A TOOL

## Slide 27: EVOLUTION OF A TOOL Hybrid Excel / CBE Tool

## Slide 28: EVOLUTION OF A TOOL Grasshopper Tool 1.0

## Slide 29: EVOLUTION OF A TOOL Grasshopper Tool 1.0

## Slide 30: EVOLUTION OF A TOOL Web Tool 1.0

## Slide 31: EVOLUTION OF A TOOL Fast, Simple Web Tool Slower, Advanced Grasshopper Tool

## Slide 32: EVOLUTION OF A TOOL Form Inputs + Buttons Component-Based Inputs Accepting a Wide Range of Data Types

## Slide 33: EVOLUTION OF A TOOL Open Source Javascript Open Source Python

## Slide 34: EVOLUTION OF A TOOL Fast Calculations for Orthogonal Geometry Slower Calculations for All Geometry

## Slide 35: ladybug web tools http://www.ladybug.tools/ladybug-web/analemma-3d/analemma-3d-r18.html three.js, google maps

## Slide 36: A Dilemma of Analemmas
Bring daily Sun path calculations anywhere in the world down to a human - ie your - level and then display results in interactive 3D in your browser -- all free and open source
Notes: An Analemma is a diagram showing the motion of the Sun in the sky, as viewed from a fixed location on the Earth.
If you can calculate the analemma for any location on earth then you can derive many useful calculations helpful in the building simulations.
The objective of this presentation is to show you that it gets easier and easier to create analemmas.
In turn this means we can get the effort out of the brains of mathematicians and programmers and into the hands of peeps like you
So you can create innovative applications for this knowledge

## Slide 37: Want this - fast, easy, simple
Notes: Show live example if possible

## Slide 38: Where is the Sun going to be?
Perhaps the oldest science/math question there is...
Antikythera Mechanism
Greek analog computer 100 BC
Stonehenge
aligned to winter solstice sunset
Sextant
Find angle between 2 objects
Notes: Calculating the position of the sun in the future is one of - if not the - oldest STEM questions in existence
Three examples you probably already know about:
Antikythera Mechanism - an orrery used to predict astronomical positions and eclipses for calendrical and astrological purposes
Stonehenge - long studied for its connections with ancient astronomy. The site is aligned in the direction of the sunrise of the summer solstice and the sunset of the winter solstice.
Sextant - The angle and the time when measured used to calculate a position line on a chart - for example, sighting the Sun at noon to estimate latitude
Today we can put these devices aside because of our laptops and phones

## Slide 39: Today Sun position is an app
Many fun apps - mostly closed source, unverifiable and with little data sharing
Notes: Today finding the position of the Sun is child’s play
Many apps out there.
Difficult if not impossible to see the source code - to verify the accuracy or quality of the code
Little or no way to import and export data
Looking for free open source tools

## Slide 40: Source code: lots of it
You can calculate Solar path - in just about any language under the Sun
We want more - and want it free and open source:
To provide you with the position of the Sun - the azimuth ( apparent longitude ) and altitude ( apparent latitude ) - quickly and easily
  Given the latitude, longitude, data and time
  Usable in any number of ways
Code that is readable by people with little programming experience
Code that is readable by people with little astronomy experience
Code that is readable by people with little experience of Euler notation
Output in interactive 3D | Share data with other apps
Notes: There’s source code for calculating Sun path in C, Basic, Fortran, Python, Swift - whatever
Yada Yada
But interactive, client-side 3D kind of limits you to JavaScript

## Slide 41: Looked at 3 JavaScript scripts
Half dozen code bases out there. Three looked at closely
Vladimir Agafonkin - SunCalc.js
Mike Bostock - Solar Calculator
National Oceanic and Atmospheric Administration (NOAA) - Solar Calculator
All good but all have issues
Notes: In 2016 we looked a good number JavaScript code bases
We discarded any code that is only available in a minified version or not FOSS
This includes http://andrewmarsh.com/apps/releases/sunpath3d.html

## Slide 42: Agafonkin: SunCalc.js
function solarMeanAnomaly(d) { return rad * (357.5291 + 0.98560028 * d); }
function eclipticLongitude(M) {
var
C = rad * (1.9148 * sin(M) + 0.02 * sin(2 * M) + 0.0003 * sin(3 * M)),//equation of center
P = rad * 102.9372; // perihelion of the Earth
return M + C + P + PI;
}
Many excellent features but
Least descriptive variables, Issues with use of UTC time
Least accurate by a long shot

## Slide 43: Bostock: Solar Calculator
(function() {
var J2000 = Date.UTC(2000, 0, 1, 12),
π = Math.PI,
τ = 2 * π,
radians = π / 180,
degrees = 180 / π;
Based on NOAA calculator
External dependency: on D3.js
Uses UTF-8 encoding - which is nice - but then embeds Greek characters - which is also cool - but very difficult to work with
Notes: If your text editor is not set up for UTF-8, the characters appear as boxes

## Slide 44: NOAA: Solar Calculator
function calcAzEl(output, T, localtime, latitude, longitude, zone) { var eqTime = calcEquationOfTime(T) var theta = calcSunDeclination(T) if (output) { document.getElementById("eqtbox").value = Math.floor(eqTime*100 +0.5)/100.0 document.getElementById("sdbox").value = Math.floor(theta*100+0.5)/100.0 }
Does not provide negative elevations
Requires the existence of specific HTML tags with specific IDs in order to operate
  Too many things like this: document.getElementById("eqtbox").value = ""
  Makes the source difficult to use generically
Variable names not coordinated and often devoid of meaning
Function names not coordinated
Generally styled and coded in a slightly archaic fashion
Provides functions with useful results but provides no easy access to those functions

## Slide 45: Ladybug Web: solarCalculator
We decided to build our own calculator
Based on Agafonkin/Bostock/NOAA efforts
Maintained on GitHub
Working hard to make the code highly readable
Working hard to provide authoritative sources for every aspect of the work

## Slide 46: Code
// https://en.wikipedia.org/wiki/Equation_of_time
function equationOfTime( century ) {
var e = eccentricityEarthOrbit( century );
var y = Math.pow( Math.tan( obliquityCorrection( century ) / 2 ), 2 );
var m = solarGeometricMeanAnomaly( century );
var l = solarGeometricMeanLongitude( century );
var sin = Math.sin, cos = Math.cos;
return y * sin( 2 * l )
- 2 * e * sin( m )
+ 4 * e * y * sin( m ) * cos( 2 * l )
- 0.5 * y * y * sin( 4 * l )
- 1.25 * e * e * sin( 2 * m );
}

## Slide 47: Shadow Range Calcs & More
Let the sun shine in...
Notes: Live demo if possible
A typical application of a Solar calculator is to show the shadows cast over the course of a day

## Slide 48
Outline:
  Examples (25 min)
    Mostapha :: epwmap
    Matt :: epwvis
    Chris :: Payette Thermal Comfort Tool
    Theo :: ladybug-web
  Workshop (40 min)
    Choosing a language for your project
  Closing & Questions (10 min)

## Slide 49: Choosing a language for your project
I want to:
Simple stuff, e.g. parse a bunch of files → Python, Ruby
Execute a bunch of commands → Bash/Shell script
Write an OpenStudio measure → Ruby OpenStudio API
Write a web application → Javascript, CSS, PHP, Python, Ruby
Make a web visualization → d3.js (javascript)
Make a 3D web visualization → three.js (javascript)
Work with applications (e.g. Revit, Unity) → C#, Visual Basic .Net
Run a bunch of statistics on my data → R, Python with pandas package
Do lots matrix calculations → C++
Write Apps for smartphones → Objective-C, Java, C++

## Slide 50: Workshop (40 min)
http://blockbuilder.org/
Get out your computers and follow along!
Topics:
Basic data binding
Exporting and using data in .json format
Calculations with .json data
Overlaying data on 3D objects

## Slide 51
Outline:
  Examples (25 min)
    Mostapha :: epwmap
    Matt :: epwvis
    Chris :: Payette Thermal Comfort Tool
    Theo :: ladybug-web
  Workshop (40 min)
    Choosing a language for your project
  Closing & Questions (10 min)

## Slide 52
Questions?
Online Resources:
Most popular programming languages:
  http://www.tiobe.com/tiobe_index
  http://githut.info/
  ***Just because a language is popular doesn’t mean it is a good fit for your task!!!
Programmer competency matrix:
  http://sijinjoseph.com/programmer-competency-matrix/
Programming resources:
  https://wiki.lesswrong.com/wiki/Programming_resources
Google

## Slide 53
Bio::Mostapha Roudsari
Mostapha Sadeghipour Roudsari is a designer, software developer, and an educator focused on the integration of parametric environmental analysis and architectural design. He is the creator of the well-known open source environmental plugins Ladybug, Honeybee, and Butterfly and web applications such as epwmap and Pollination. He lectures and teaches seminars frequently throughout Architecture and Engineering schools, the AEC community, and as a lecturer at the University of Pennsylvania.

## Slide 54
Bio::Mathew Dahlhausen
Matthew Dahlhausen is an Energy Modeler with Integral Group, Inc. He is the team's expert on OpenStudio, parametric modeling, scripting, data analysis, and data visualization with web tools. In addition to his work, he is pursuing his doctorate in Mechanical Engineering at the University of Maryland, focusing on building energy model calibration. He holds an M.S. in Architectural Engineering from Penn State, and a B.E. in Environmental Engineering from Dartmouth College. He has authored or co-authored several papers in the field.

## Slide 55
Bio::Chris Mackey
Chris has worked as a Building Scientist at Payette Architects since 2015 after finishing both his Masters of Architecture and Masters of Science in Building Technology at MIT. He is one of the primary developers of the Ladybug + Honeybee environmental analysis plugins for Rhino/Grasshopper, which are regularly applied at Payette and across the globe by a community of over 70,000 people.

## Slide 56
Bio::Theo Armour
Theo was awarded a BA from Syracuse University in New York and an AADip - equivalent to an MS - from the Architectural Association in London. He has been a licensed architect - and practiced in the UK renovating houses and in Hong Kong designing twelve underground mass transit stations.
While working at Autodesk for ten years, he was program manager for three releases of AutoCAD - the market leading application for computer aided design.
He is currently an angel investor and technical mentor for a number of startups. He is a software developer who makes extensive use of the Three.js JavaScript library. He is a maintainer of the Three.js and WebGL subreddits at www.reddit.com. He is a principal author of the Three.js Wikipedia entry.